## Slide 1
COMBATING VEHICULAR POLLUTION: GETTING BEYOND RECITATION
Dr. Prashant Gargava and Ms Meetu Puri
Central Pollution Control Board
Delhi
(Email: eepg.cpcb@nic.in)
(Web: http://www.cpcb.nic.in)
ICAMP: POLICY CONCLAVE ON REDUCING VEHICULAR EMISSIONS TO IMPROVE AIR QUALITY
DELHI, FEBRUARY 04, 2014

## Slide 2
PRESENTATION OUTLINE
VEHICULAR POLLUTION CONTROL
What have been done? – Actions
What have been achieved? – Status
Are we on the right track? – Action Dilemma
What can be done? – Way Forward

## Slide 3
VEHICULAR POLLUTION CONTROL
TECHNOLOGY INTERVENTIONS
Improved fuel quality – S content in Diesel: 0.5% (1996) – 0.005% (mega cities) and 0.035% (rest of the country) (2010); Gasoline: 0.015% – 0.005%
Progressive emission norms for vehicles – BS I (1999) – BS IV in major cities and BS III in rest of the country (2010)
Alternate cleaner fuel (CNG/LPG) – 1.1 million vehicles (8% of total fleet), 0.55 million in Delhi
Improvement in public transport system (Metro) – 2.5 million passengers; 2500 trips covering 69,000 km
RESOURCE INTENSIVE

## Slide 4
BS-III
BS-IV
BS-V
BS-VI
CO
HC+NOx
NOx
PM
0.64
0.50
0.50
0.50
0.56
0.30
0.23
0.17
0.50
0.25
0.18
0.08
0.05
0.025
0.005
0.005
21.8%
0%
0%
46.4%
23.3%
26%
50%
28%
55.5%
80%
50%
0%
EMISSION REDUCTIONS IN PASSENGER CARS ( DIESEL)

## Slide 5
BS-III
BS-IV
BS-V
BS-VI
CO
HC
NOx
2.3
1.0
1.0
1.0
0.20
0.10
0.10
0.10
0.15
0.08
0.06
0.06
21.8%
0%
0%
50.0%
0%
0%
47%
25%
0%
EMISSION REDUCTIONS IN PASSENGER CARS (GASOLINE)

## Slide 6
VEHICULAR POLLUTION CONTROL
MANAGEMENT INTERVENTIONS
Phasing out of old commercial vehicles
PUC Scheme
Restriction on goods vehicles during day time
Installation of time clocks at important crossings
Construction of more flyovers and subways
IMPLEMENTATION DIFFICULTIES

## Slide 7
Source : MoRTH & Delhi Transport Department
VEHICLE GROWTH IN DELHI AND INDIA

## Slide 8
Chart: Year
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011
Vehicle | 3353038 | 3456579 | 3551690 | 3940409 | 4202455 | 4508026 | 4809010 | 5185410 | 5627384 | 6011731 | 6451883 | 6932706 | 7438155
Nox | 60.0833 | 58.9167 | 67 | 75 | 94 | 89 | 83 | 78 | 72 | 58.6741 | 78.3458 | 63.326 | 68.6192
PM 2.5 | 31 | 40 | 40 | 33 | 41
PM10 | 215.75 | 190.5 | 180 | 270 | 244 | 228 | 259 | 220 | 211 | 211.4081 | 212.6717 | 231.9391 | 196.3676
AIR QUALITY AT ITO, DELHI

## Slide 9
SIX CITY STUDY: PM10 SOURCE CONTRIBUTIONS
City | Bangalore | Chennai | Delhi | Kanpur | Mumbai | Pune
Sources |  |  |  |  |  | 
Roadside Dust | 45 – 55 | 6 – 27 | 14 – 29 | 7 – 9 | 29 – 47 | 49 – 64
Vehicles | 10 – 22 | 35 – 48 | 9 – 20 | 15 – 17 | 8 – 26 | 2 – 10
Industries | 27 | - | 6 – 9 | 2 – 19 | 1 – 7 | -
Construction | - | - | 23 | - | 28 – 46 | 6 – 28
Secondary Particulates | 2 – 11 | - | - | 16 – 19 | 10 – 21 | -
Domestic | - | 4 – 20 | 3 – 9 | 15 – 26 | 3 – 18 | -
DG Sets | 7 – 18 | 14 – 16 | 7 – 12 | 5 – 8 | - | 3 – 4
Roadside dust and vehicles are prominent sources in all the six cities

## Slide 10
  EMISSION INVENTORY FOR SIX CITIES
PM10:
Major Source – Road dust re-suspension
Significant contribution of industries in Kanpur, Mumbai and Delhi
NOx:
Vehicles are major source
Contribution of industries (power plants) high in Delhi, Mumbai and Kanpur
Important observation: A few prominent sources in a city can mask the contribution of the other sources.
HEAVY DUTY DIESEL VEHICLE: 40 – 59%

## Slide 11
EMISSION INVENTORY (TONS/YEAR): DELHI, 2010
Source: International Council on Clean Transportation

## Slide 12
Chart: 
| PM10 | EC | OC | TC | Pb | Ni | As
Power Plant | 25296 | 475.1736 | 2203.093 | 2678.2666 | 25.2663 | 22.7557 | 6.5363
Industry | 2233 | 326.8095 | 185.2188 | 512.0284 | 0.63026 | 5.7408 | 0.43061
Domestic Cooking | 11600 | 937.9182 | 5509.096 | 6447.0141 | 56.7561 | 3.0623 | 13.6168
Commercial | 271.69 | 15.6254 | 99.507 | 115.1324 | 1.2467 | 0.10745 | 0.57668
Crematoria | 1300 | 103.9819 | 629.7862 | 733.7681 | 6.1216 | 0.28956 | 1.3708
Waste Incinerator | 17 | 0.3128 | 12.9262 | 13.239 | 0.50084 | 0.0022892 | 0.0017217
Soild Waste Burning | 1.4 | 0 | 0.72883 | 0.74899 | 0.00023496 | 1.1034e-05 | 5.3353e-05
Construction | 12290 | 174.943 | 1080.696 | 1255.6389 | 5.3262 | 0.91161 | 0.72077
Generator Set | 534 | 88.8544 | 213.3063 | 302.1607 | 0.56353 | 0.28088 | 0.39682
Paved Road | 77275 | 2173.0845 | 7094.535 | 9267.6195 | 104.5643 | 9.9054 | 2.5103
Vehicle | 9700 | 2104.2969 | 4773.0515 | 6877.3484 | 1.7277 | 0.12469 | 0.08138
CARBON AND TOXIC METAL FRACTION IN PM10 EMISSIONS IN DELHI, 2007: CONTRIBUTION OF DIFFERENT SOURCES

## Slide 13
Chart: 
| PM10 | EC | OC | TC | Pb | Ni | As
Liquified Petroleum Gas | 790 | 22.2856 | 183.3848 | 205.6704 | 3.5221 | 0.4391 | 2.5895
Compressed Natural Gas | 1044.6 | 58.5288 | 377.589 | 436.1179 | 0.53046 | 0.4221 | 0.028393
Gasoline | 1242 | 55.6871 | 607.6504 | 663.3375 | 0.93282 | 0.032898 | 0.027164
Diesel | 7242.4 | 2110.8177 | 3951.9316 | 6062.7493 | 1.1306 | 5.6519 | 0.87864
Kerosene | 101.4 | 55.3953 | 267.5454 | 322.9407 | 0.44419 | 0.30767 | 0.20976
Coal | 25520.29 | 492.7192 | 2320.6154 | 2813.3345 | 28.8787 | 22.7876 | 6.5694
Wood | 12050 | 963.8323 | 5837.6339 | 6801.4662 | 56.7425 | 2.684 | 12.7066
CARBON AND TOXIC METAL FRACTION IN PM10 EMISSIONS IN DELHI, 2007: CONTRIBUTION OF DIFFERENT FUELS

## Slide 14
Chart: 
| PM10 | EC | OC | TC | Pb | Ni
Diesel Vehicle | 7866 | 2023.9455 | 3907.9148 | 5931.8604 | 0.71733 | 0.089427
Compressed Natural Gas Vehicle | 592 | 24.6642 | 257.4863 | 282.1505 | 0.077542 | 0.0023674
Gasoline Vehicle | 1242 | 55.6871 | 607.6504 | 663.3375 | 0.93282 | 0.032898
CONTRIBUTION OF DIESEL, GASOLINE AND CNG FUELED VEHICLES TO PM10, CARBON AND TOXIC METAL EMISSIONS IN DELHI, 2007

## Slide 15
Action Dilemma – Technology v/s Management based options?
No direct visible impact/correlation of the measures taken – many influencing factors
Many contributing sources – vehicle share not most prominent, but road dust could be attributed to vehicle movement
Higher contribution of vehicles and diesel in toxic carbon component of PM
CONCLUSION

## Slide 16
Efficient, affordable, convenient public transport
Next generation norms – sooner the better
Get the dirty vehicles off the roads as quickly as possible
Address pollution from heavy duty diesel vehicles – effective freight management
Policies to translate in micro level actions
Minimize activities in hotspots
Experiment with ideas
Aggressive public awareness
WAY FORWARD
HOW AND HOW FAST??

## Slide 17
THANK YOU